## Slide 1: FlowConX
Risk-controlled throughput forecasting and bandwidth allocation for Starlink (LEO satellite) access links
Mayan Sharma (23BAI1581) Kriti Saini (23BCE1520) Devansh Behl (23BCE1334)
Guide: Dr. Suganya R, Professor, SCOPE
Industry mentor: Mr. S. Vijayaragavan, Professor of Practice, Nelco Network Products Ltd.
School of Computer Science and Engineering, Vellore Institute of Technology
Notes: FlowConX forecasts how much a Starlink link can safely carry, and uses that to decide how many sessions to admit, when to raise a congestion alert, and which flow to slow down when capacity is short.

## Slide 2: Domain Knowledge and Problem Understanding
The problem
Starlink capacity changes every 15 s: the network reschedules users at seconds 12, 27, 42 and 57 of each minute, and satellites hand over constantly.
An operator must commit bandwidth before it knows what the link will carry. Over-promise and sessions drop; under-promise and paid capacity sits idle.
Industry brief: predict degradation, detect congestion early, allocate bandwidth automatically. We chain four needs into one system, adding: decide which flow is slowed when capacity is short.
Prior work
StarNet (Liu et al., CoNEXT 2025): point forecast of throughput.
BG-CFQS (Xie et al., 2026): safe lower bound from one global quantile.
Casparsen et al. (2026): the 15 s scheduling period. Horizon (SIGMETRICS 2026): global Starlink performance.
Chart: BG-CFQS: how often the bound over-promises (budget 0.35)
| All decisions | Lowest 30% of throughput | Lowest 10% of throughput
value | 0.34 | 0.671 | 0.848
Our reproduction of BG-CFQS. The risk is held on average and lost exactly where capacity is lowest, which is where over-allocation drops sessions.
Notes: Key point: the published state of the art controls risk on average but not in the low-capacity moments that matter. That gap motivated the project.

## Slide 3: Methodology, Architecture and Technical Design
Data flow: each layer only talks to the one below it, so each can be tested on its own.
Ingest
Starlink traces at 1 Hz: throughput, serving satellite, elevation, distance, satellites in view, weather
State
11-feature vectors; 15 s phase recovered by edge detection, not hardcoded
Forecast
StarNet GRU encoder-decoder with periodic embedding and attention; 30 s in, 5 s out
Calibrate
Point forecast to safe lower bound; online update keeps over-promising at budget ε
Decide
Admission control, congestion alert, and flow protection, all from the one bound
Serve
FastAPI WebSocket, one decision per second, to a terminal console
Algorithms
Online conformal calibration: after each outcome, α ← α + γ(ε − err), so the bound tracks the budget as the link drifts.
Admission: floor(bound / 10 Mbps) sessions. Congestion: bound below the committed rate for 5 decisions in a row.
Flow protection: criticality scored online from 7 signals (attention, interactivity, elasticity, deadline, irreversibility, volume, recurrence), then the bound is split by weighted max-min fairness with protected minimums.
Technical decisions
Temporal train / calibration / test splits. Random splits flatter these models.
The calibration set is used only to set the operating point, never to fit.
Congestion is derived from the bound, not a separate classifier.
No flow is ever cut to zero while capacity remains.
Every run saves its configuration and seed.
Notes: Walk the pipeline left to right. The bound produced by Calibrate is the single number every decision is made from.

## Slide 4: Completion, Functionality and Integration
Module | What it delivers | Status
Throughput forecast | StarNet reproduced on USA, Canada, Germany | Complete
Safe bound | Online calibration at any risk budget | Complete
Admission control | Sessions admitted from the safe bound | Complete
Congestion alert | Early warning from the same bound | Complete
Flow protection | Decides which flow is slowed, never stopped | Complete
Latency, availability, cost | Measured beyond the approved scope | Complete
Live system | ML service and terminal console on real traces | Complete
Integration at run time
Recorded Starlink trace (real Canada data)
ML service: forecast, bound, decisions
Terminal console: ML monitor and flow protection screens
WebSocket, 1 decision/s
Runs end to end on a laptop; the replay loops continuously without restarts.
328 automated tests pass on every change.
Notes: Then switch to the live demo: m for the ML monitor, p for flow protection.

## Slide 5: Testing, Validation and Analysis of Results (1/2)
How it was tested
Reproduce the published baselines first; no new method until both match.
Temporal splits and leave-one-location-out across USA, Canada and Germany, plus a second measurement campaign (WetLinks).
Data loader checked against published sample counts: 145,053 (Canada), 613,295 (Germany), 1,123,832 (USA), all exact.
328 automated tests, including checks that no decision uses future data.
Every number is read from a saved result with its configuration and seed.
Reproduction against published results
Check | Published | FlowConX
StarNet RMSE, average (Mbps) | 39.30 | 39.73 (+1.1%)
StarNet MAE, average (Mbps) | 29.28 | 29.97 (+2.4%)
BG-CFQS over-promise rate | 0.349 | 0.340
BG-CFQS, lowest 30% | 0.65 to 0.71 | 0.671
BG-CFQS, lowest 10% | 0.83 to 0.86 | 0.848
15 s phase offset (s) | 12 | 11.98 / 12.09 / 12.25
Both reproduction checks passed. Per-location StarNet gaps scatter in both directions (4.2% to 6.9%), as an independent reimplementation should.
Notes: The phase offset row: three continents, recovered from 1 Hz throughput, against the 12 s published from 500 Hz latency probes.

## Slide 6: Testing, Validation and Analysis of Results (2/2)
Chart: Critical flows allocated below their minimum (lower is better)
| Perfect classification (oracle) | FlowConX | Throttle the largest | Equal share | Class priority (DiffServ)
value | 0.029 | 0.065 | 0.218 | 0.251 | 0.301
Canada link, 2x load, 5 workload seeds. Critical transfers that gave up: 0.3% with FlowConX against 12.1% when the largest flow is throttled first. Capacity is measured; flows are simulated.
Key results
Measure | Before | FlowConX
Risk budget held (throughput) | 16% to 21% off | within 1%
Availability | about 1.2 nines | about 2.1 nines
Number of outages | baseline | 5 to 6x fewer
Latency budget 0.10 held | 0.033 to 0.313 | 0.088 to 0.101
What did not work, reported as found
Conditioning on satellite geometry did not improve risk control on StarNet.
Congestion alerts fire early but are noisy (F1 0.46).
The scorer cannot tell a video call from a video stream (precision 0.71).
BG-CFQS cannot serve budgets below 0.15 (3.7x overshoot at 0.05).
Notes: 'Before' is static calibration, or the uncalibrated forecast for availability. The negatives are deliberate: each was measured and is in the report.

## Slide 7: Innovation, Technical Merit and Practical Relevance
Contribution
First evaluation of risk-controlled capacity forecasting on LEO links: 4 datasets, 2 measurement campaigns.
Showed BG-CFQS needs exchangeable data and has a budget floor.
Flow protection splits the safe bound, so a reserved minimum is a promise that can be checked.
Feasibility
Runs on a laptop: CPU, CUDA or Apple MPS.
The demo model trains in about 75 s and decides once per second.
Uses only data a terminal has at prediction time.
Ethical responsibility
Public measurement traces; no personal data.
Simulated flows are labelled as simulated on screen.
No flow is stopped while capacity remains; self-declared priority is not trusted blindly.
Failures and withdrawn claims are reported.
Industry validation
Demonstrated live to Mr. S. Vijayaragavan, Professor of Practice, Nelco Network Products Ltd., who was very impressed with the system.
He set the problem statement and co-authored our paper with us, prepared for submission to ACM SIGMETRICS 2027.
Practical use: satellite operators can commit bandwidth at a stated risk and keep critical traffic, such as a hospital upload, running when the link is short.
Notes: Be precise about the claim: the mechanisms are published and cited; what is new is the evaluation and what it found, plus coupling flow protection to a calibrated bound.